## Slide 1
Operators and Logic
Notes: Title slide. Last lecture built new types out of old ones. This lecture is about what we can DO with all of those values.

## Slide 2
Where We Left Off
A variable is one name for one value
A struct is a new type <T> built from members
An array is N instances of one type
Now: what can we do with them?
Notes: Quick review using the vocabulary from last time: a struct defines a new type <T>, and a declared variable is an instance of it.

## Slide 3
The ALU Does the Work
The ALU example did an ADD
The Operation input selects what it does
Operation
ADD SUB MUL AND OR XOR ...
1
10
9
8
7
6
5
4
2
3
ALU
result
Notes: Callback to the very first slides of the course. The same box that added our numbers can subtract, multiply, and do logic. An operator in the source code selects the operation.

## Slide 4
What an Operator Is
An operator takes the contents of its operands and produces a new value
(result) <= ( a ) + ( b ) Computer Architects view
Binary operators take two operands: a + b
Unary operators take one: -a !a
Notes: Use the ( variable ) notation from last lecture: the operator works on the contents of a and b, not on their addresses.

## Slide 5
Arithmetic Operators
+ addition
- subtraction
* multiplication
/ division
% remainder (modulo)
The same symbols in C, C++, and Rust
Notes: The easy part: the five arithmetic operators are spelled the same in all three languages. The differences are in what happens at the edges, which is the next several slides.

## Slide 6
Integer Division Truncates
7 / 2 = 3
-7 / 2 = -3
7.0 / 2.0 = 3.5
Integer division throws away the fraction
It drops the remainder
It rounds toward zero in all three languages
Notes: The classic beginner bug: average = sum / count with integers. If you want a fraction, at least one operand has to be floating point.

## Slide 7
The Remainder Operator
7 % 3 = 1
-7 % 3 = -1 sign follows the left operand
C, C++: % is for integers only
Use fmod(a, b) for floating point
Rust: % also works on f32 and f64
Notes: The negative case surprises mathematicians, who expect 2. Rust offers rem_euclid() for the always-positive version.

## Slide 8
Division by Zero
Integers:
C, C++: undefined behavior
Rust: the program panics and stops
Floating point, all three languages:
1.0 / 0.0 = inf
0.0 / 0.0 = NaN (not a number)
Notes: Undefined behavior means the language makes no promise at all. On many embedded parts integer divide by zero silently returns garbage rather than crashing.

## Slide 9
Increment and Decrement
C, C++:
x++ ; add one
x-- ; subtract one
Rust has no ++ or –
You will need to use the compound operators
x += 1 ;
x -= 1 ;
Notes: Rust dropped ++ deliberately, to remove the prefix/postfix confusion on the next slide.

## Slide 10
Prefix and Postfix
x = 5 ; y = x++ ; y is 5, x is 6
x = 5 ; y = ++x ; y is 6, x is 6
Postfix: use the value, then add one
Prefix: add one, then use the value
Never use x++ twice in one expression
Notes: i = i++ + ++i is undefined behavior in C. The safe habit is to use ++ only as a statement on its own line.

## Slide 11
Compound Assignment
x += 5 ; (x) <= ( x ) + 5
x -= 5 ; (x) <= ( x ) - 5
x *= 5 ; (x) <= ( x ) * 5
x /= 5 ; (x) <= ( x ) / 5
x %= 5 ; (x) <= ( x ) % 5
Same in C, C++, and Rust
Notes: Read the right column out loud in the course notation: x receives the contents of x plus five. The bit operators get the same shorthand later.

## Slide 12
Overflow in C and C++
uint8_t x = 255 ;
x = x + 1 ; x is now 0
Unsigned overflow wraps around - defined
Signed overflow is undefined behavior
int8_t y = 127 ; y + 1 -> ???
Notes: Tie back to machine size: an 8 bit register cannot hold 256. Unsigned arithmetic is defined as modulo 2^n; signed overflow lets the optimizer assume it never happens.

## Slide 13
Overflow in Rust
let x : u8 = 255 ;
let y = x + 1 ;
Debug build: panics - overflow is caught
Release build: wraps to 0
Say what you mean: returns
x.wrapping_add(1) 0
x.checked_add(1) None
x.saturating_add(1) 255
Notes: Rust makes you choose the behavior explicitly. saturating is what you usually want for a sensor value; wrapping is what you want for a counter or a checksum.

## Slide 14
Mixing Types in C and C++
uint8_t a = 200, b = 100 ;
int d = a + b ; 300
uint8_t c = a + b ; 44
Small types are promoted to int first
The result is cut down when stored
Notes: This is integer promotion. 300 does not fit in 8 bits, so storing it keeps only the low byte: 300 - 256 = 44. No warning by default.

## Slide 15
Mixing Types in Rust
let a : u8 = 200 ;
let d : i32 = a + 1000 ; error
Rust never converts types for you
You convert explicitly with as:
let d : i32 = a as i32 + 1000 ;
Notes: More typing, but every conversion is visible in the source. The C bug on the previous slide cannot happen silently in Rust.

## Slide 16
Floating Point is Not Exact
0.1 + 0.2 == 0.3 false
Most decimals cannot be stored exactly in binary
Compare with a tolerance instead:
fabs(a - b) < 1e-6 C, C++
(a - b).abs() < 1e-6 Rust
Notes: 0.1 in binary is a repeating fraction, like 1/3 in decimal. Never test floats with ==.

## Slide 17
Comparison Operators
== equal
!= not equal
< less than <= less or equal
> greater than >= greater or equal
The result is true or false
C: an int, 1 or 0
C++, Rust: a bool
Notes: Same symbols in all three languages. C predates bool, so comparisons produce int.

## Slide 18
= is not ==
if ( x = 5 ) assigns 5, then tests it
always true in C and C++
if ( x == 5 ) tests whether x is 5
Rust refuses to compile the first one
an assignment is not a bool
Notes: One of the most famous bugs in C. Compilers warn about it with -Wall, which is another reason to always build with warnings on.

## Slide 19
Chained Comparisons
Mathematics: 0 < x < 10
C, C++: compiles, and is wrong
( 0 < x ) is 0 or 1 - always < 10
Rust: compile error
Write: 0 < x && x < 10
or better yet
(0 < x) && (x < 1)
Notes: This one is caught by Rust and silently accepted by C. The && operator is coming up in the logic section.

## Slide 20
Operators on Struct Members
A member is an ordinary variable
Every operator works on it:
my_sample.psi * 2.0
my_sample.adc_counts + 1
my_sample.timestamp_ms - start
Same in C, C++, and Rust
Notes: The member access happens first, producing an ordinary value of the member type, then the operator applies. Nothing new here, which is the point.

## Slide 21
Assigning a Whole Struct
C, C++:
sample_t sample2 ;
sample2 = my_sample ; copies every byte
Rust:
let sample2 = my_sample ; moves it
my_sample can no longer be used
Add #[derive(Clone, Copy)] to copy instead
Notes: Assignment is the one operator that works on a whole struct in every language. Ownership is a forward reference; one sentence is enough here.

## Slide 22
Comparing Structs in C
if ( my_sample == sample2 ) compile error
Compare member by member:
my_sample.adc_counts == sample2.adc_counts
&& my_sample.psi == sample2.psi
&& my_sample.timestamp_ms == sample2.timestamp_ms
Do not use memcmp - it compares the padding too
Notes: The padding bytes from last lecture hold garbage, so two structs with equal members can still differ byte for byte.

## Slide 23
Comparing Structs in C++
Ask the compiler to write == for you (C++20):
struct sample {
uint32_t adc_counts ;
float psi ;
uint64_t timestamp_ms ;
bool operator == (const sample&) const = default ;
} ;
Overloads == operator
Now my_sample == sample2 compares every member
// What the compiler effectively generates:
bool operator == (const sample& other) const {
return (adc_counts == other.adc_counts) &&
(psi == other.psi) &&
(timestamp_ms == other.timestamp_ms) ;
}
Notes: Before C++20 you wrote operator== by hand. This is the first taste of operator overloading: C++ lets a type define what an operator means for it.

## Slide 24
Comparing Structs in Rust
#[derive(PartialEq)]
struct Sample {
adc_counts : u32,
psi : f32,
timestamp_ms : u64,
}
Now my_sample == sample2 compares every member
Notes: derive asks the compiler to generate the comparison. PartialEq rather than Eq because f32 has NaN, which is not equal to itself.

## Slide 25
Arithmetic on Whole Structs
my_sample + sample2 ??
No language can guess what + means for your type
C: not possible - write a function
C++: define operator +
Rust: implement the Add trait
This is operator overloading - later lecture possibly
(not a great idea IMHO)
Notes: Plant the idea only. Adding two samples does not even make sense; adding two vectors does, which is where overloading earns its keep.

## Slide 26
Operators on Array Elements
An element is an ordinary variable
Every operator works on it:
counts[i] + 1
psi[i] * scale
history[7].psi - history[6].psi
Same in C, C++, and Rust
Notes: Same message as for struct members: index first, then operate. The last line combines an array of structs with a member and an operator.

## Slide 27
Whole Arrays in C
uint32_t a[4], b[4] ;
a = b ; compile error
if ( a == b ) compares addresses, not contents
Copy with: memcpy(a, b, sizeof(a)) ;
Compare with: a loop, or memcmp
Notes: The array name decays to a pointer to element 0. So a == b asks whether the two arrays live at the same address, which they never do.

## Slide 28
Whole Arrays in C++
#include <array>
std::array<uint32_t, 4> a, b ;
a = b ; copies every element
if ( a == b ) compares every element
Another reason to prefer std::array
Notes: std::array behaves like a value, the way students expect an array to behave.

## Slide 29
Whole Arrays in Rust
let a : [u32 ; 4] = [1, 2, 3, 4] ;
let mut b : [u32 ; 4] = [0 ; 4] ;
b = a ; copies every element
if a == b { ... } compares every element
Works because the length is part of the type
Notes: Rust arrays are values. The compiler knows both lengths, so it can compare them safely.

## Slide 30
Element-wise Math Needs a Loop
C, C++:
for ( int i = 0 ; i < 4 ; i++ ) {
sum[i] = a[i] + b[i] ;
}
Rust:
for i in 0..4 {
sum[i] = a[i] + b[i] ;
}
Notes: None of the three languages has a + for whole arrays. This is exactly what a vector math library provides - and what hardware SIMD instructions do in one step.

## Slide 31
Two Kinds of Logic
Clause level
combines conditions that are true or false
if ( psi < 10.0 || psi > 80.0 )
Bit level
applies logic to every bit of an integer
status & 0x80
Notes: Frame the rest of the lecture. Same Boolean logic, two different scales: whole conditions, or each bit independently.

## Slide 32
What Counts as True
C: 0 is false, anything else is true
if ( count ) means if ( count != 0 )
C++: bool, but numbers convert silently
Rust: only a bool is a condition
if count { } compile error
if count != 0 { } correct
Notes: C inherited this from assembly, where branch-if-zero is the natural test. Rust makes you write the comparison, which removes a class of bugs.

## Slide 33
Logical Operators
&& AND true if both are true
|| OR true if either is true
! NOT flips true and false
The same symbols in C, C++, and Rust
if ( psi < 10.0 || psi > 80.0 ) alarm() ;
Notes: These operate on whole conditions. The result is 1/0 in C and a bool in C++ and Rust.

## Slide 34
Short-Circuit Evaluation
a && b if a is false, b is never evaluated
a || b if a is true, b is never evaluated
This makes guards safe:
if ( count != 0 && total / count > 10 )
Division by zero cannot happen
Notes: Evaluation is left to right and stops as soon as the answer is known. In C the same idiom guards pointers: if ( p != NULL && p->psi > 50.0 ).

## Slide 35
Boolean Logic
George Boole, 1854: logic as algebra
Two values: 0 and 1 (false and true)
Every operation is defined completely by a
truth table: one row for every input combination
Two inputs -> 4 rows
Notes: This is where the EE and CS halves of the curriculum meet. The same seven tables describe the gates in a chip and the operators in a program.

## Slide 36
NOT
Y = A'
Flips the input
Clause level:
!a all three
Bit level:
~a C, C++
!a Rust
A
Y
0
1
1
0
Notes: Also written with a bar over A. The only one-input operation. Note that Rust spells bitwise NOT with ! - it has no ~ operator.

## Slide 37
AND
Y = A · B
1 only when both inputs are 1
Clause level:
a && b all three
Bit level:
a & b all three
A
B
Y
0
0
0
0
1
0
1
0
0
1
1
1
Notes: AND is multiplication on 0 and 1, which is why it is written with a dot.

## Slide 38
OR
Y = A + B
1 when either input is 1
(or both)
Clause level:
a || b all three
Bit level:
a | b all three
A
B
Y
0
0
0
0
1
1
1
0
1
1
1
1
Notes: Inclusive or. In English "or" is often exclusive; in logic it is not.

## Slide 39
NAND
Y = (A · B)'
NOT of AND: 0 only when
both inputs are 1
Clause level:
!(a && b) all three
Bit level:
~(a & b) C, C++
!(a & b) Rust
A
B
Y
0
0
1
0
1
1
1
0
1
1
1
0
Notes: No language has a NAND operator - you compose it. In hardware NAND is the cheapest gate to build in CMOS, which is why it matters so much.

## Slide 40
NOR
Y = (A + B)'
NOT of OR: 1 only when
both inputs are 0
Clause level:
!(a || b) all three
Bit level:
~(a | b) C, C++
!(a | b) Rust
A
B
Y
0
0
1
0
1
0
1
0
0
1
1
0
Notes: Like NAND, NOR is universal - every other gate can be built from it alone.

## Slide 41
XOR
Y = A  B
1 when the inputs differ
Clause level:
a != b C, C++
a ^ b Rust (bool)
Bit level:
a ^ b all three
A
B
Y
0
0
0
0
1
1
1
0
1
1
1
0
Notes: Exclusive or. C has no logical XOR operator; != works when both sides are already 0 or 1. For arbitrary ints in C, write !a != !b. XOR is also a one-bit adder without the carry.

## Slide 42
XNOR
Y = (A  B)'
1 when the inputs are equal
Clause level:
a == b all three
Bit level:
~(a ^ b) C, C++
!(a ^ b) Rust
A
B
Y
0
0
1
0
1
0
1
0
0
1
1
1
Notes: XNOR is the equality gate. A comparator that checks two numbers for equality is a row of XNOR gates feeding one big AND.

## Slide 43
All Seven Together
A
B
NOT A
AND
OR
NAND
NOR
XOR
XNOR
0
0
1
0
0
1
1
0
1
0
1
1
0
1
1
0
1
0
1
0
0
0
1
1
0
1
0
1
1
0
1
1
0
0
0
1
NOT uses only A. The shaded columns are outputs.
Notes: Have students photograph this one. Read down a column to see an operation; read across a row to see all seven answers for the same inputs.

## Slide 44
NAND Can Build Everything
NOT A = A NAND A
A AND B = NOT ( A NAND B )
A OR B = ( NOT A ) NAND ( NOT B )
NAND is universal
A whole computer can be built from one kind of gate
Notes: Worth checking one line against the truth tables together in class. This is the bridge to digital logic courses.

## Slide 45
De Morgan's Laws
NOT ( A AND B ) = ( NOT A ) OR ( NOT B )
NOT ( A OR B ) = ( NOT A ) AND ( NOT B )
In code:
!(a && b) == !a || !b
!(a || b) == !a && !b
Flip every operator and negate every term
Notes: Useful every day for rewriting a condition so it reads naturally: "not (in range)" becomes "below the minimum or above the maximum".

## Slide 46
Bitwise Operators
& AND all three
| OR all three
^ XOR all three
~ NOT C, C++
! NOT Rust
<< shift left all three
>> shift right all three
Each bit column is computed independently
Notes: Now the same logic applied to every bit of an integer at once. One instruction, eight or thirty-two or sixty-four gates working in parallel.

## Slide 47
Bitwise AND
Each column is one row of the AND truth table
Result bit is 1 only where both bits are 1
7
6
5
4
3
2
1
0
a
1
1
0
0
1
0
1
0
0xCA = 202
b
1
1
1
1
0
0
0
0
0xF0 = 240
a & b
1
1
0
0
0
0
0
0
0xC0 = 192
Notes: Point at one column and read it as a row of the AND table. b here acts as a mask that keeps the top four bits of a and clears the bottom four.

## Slide 48
Bitwise OR
Each column is one row of the OR truth table
Result bit is 1 where either bit is 1
7
6
5
4
3
2
1
0
a
1
1
0
0
1
0
1
0
0xCA = 202
b
1
1
1
1
0
0
0
0
0xF0 = 240
a | b
1
1
1
1
1
0
1
0
0xFA = 250
Notes: OR with a mask forces bits to 1. That is how you turn a bit on.

## Slide 49
Bitwise XOR
Each column is one row of the XOR truth table
Result bit is 1 where the bits differ
7
6
5
4
3
2
1
0
a
1
1
0
0
1
0
1
0
0xCA = 202
b
1
1
1
1
0
0
0
0
0xF0 = 240
a ^ b
0
0
1
1
1
0
1
0
0x3A = 58
Notes: XOR with a mask flips exactly the masked bits. XOR the result with b again and you get a back - the basis of simple checksums and ciphers.

## Slide 50
Bitwise NOT
Every bit flips
~a in C and C++, !a in Rust
7
6
5
4
3
2
1
0
a
1
1
0
0
1
0
1
0
0xCA = 202
~a
0
0
1
1
0
1
0
1
0x35 = 53
Notes: For an 8 bit value, ~a equals 255 - a. Watch out in C: ~ on a uint8_t promotes to int first, so ~a is 0xFFFFFF35 until you store it back into 8 bits.

## Slide 51
& is not &&
C: 1 & 2 = 0 bitwise: 01 & 10 = 00
1 && 2 = 1 both are non-zero
Rust: 1 & 2 = 0
1 && 2 compile error - not bool
if ( a & b ) is a different test than if ( a && b )
Notes: A one-character typo that compiles in C and changes the meaning completely. Rust catches it because && demands bool operands.

## Slide 52
Shift Left
Every bit moves one place left; a 0 enters on the right
x << n multiplies by 2 to the n
7
6
5
4
3
2
1
0
a
1
1
0
0
1
0
1
0
202
a << 1
1
0
0
1
0
1
0
0
148 (bit 7 fell off)
Notes: 202 * 2 = 404, which does not fit in 8 bits. 404 - 256 = 148: the top bit was shifted out. Shifting is how the hardware multiplies by powers of two.

## Slide 53
Shift Right
Every bit moves one place right; bit 0 falls off
x >> n divides by 2 to the n
7
6
5
4
3
2
1
0
a
1
1
0
0
1
0
1
0
202
a >> 1
0
1
1
0
0
1
0
1
101
Notes: For an unsigned value a 0 enters on the left. The next slide covers signed values.

## Slide 54
Shifting Signed Values
Unsigned: a 0 enters on the left (logical)
Signed: the sign bit is copied (arithmetic)
-8 >> 1 = -4
Rust, C++20: guaranteed arithmetic
C: implementation defined
Use unsigned types for bit work
Notes: Every mainstream C compiler does arithmetic shift, but the standard does not promise it. The simple rule: do bit manipulation on unsigned types only.

## Slide 55
Shifting Too Far
uint32_t x = 1 ;
x << 32 ??
C, C++: undefined behavior
Rust: panics in a debug build
Shift by less than the width of the type
Use 1u << n in C - never 1 << 31
Notes: 1 << 31 on a 32 bit int shifts into the sign bit, which is undefined in C. The u suffix makes the 1 unsigned and the shift well defined.

## Slide 56
Bitwise Compound Assignment
x &= m ; (x) <= ( x ) & m
x |= m ; (x) <= ( x ) | m
x ^= m ; (x) <= ( x ) ^ m
x <<= n ; (x) <= ( x ) << n
x >>= n ; (x) <= ( x ) >> n
Same in C, C++, and Rust
Notes: These are the forms you will use most when working with hardware registers.

## Slide 57
Masks
A mask is a constant that selects bits
C: #define ENABLE_BIT ( 1u << 7 )
C++: constexpr uint8_t ENABLE_BIT = 1u << 7 ;
Rust: const ENABLE_BIT : u8 = 1 << 7 ;
Constants are SCREAMING_SNAKE_CASE
in all three languages
Notes: Write the mask as a shift, not as 0x80. The reader sees immediately which bit it is.

## Slide 58
Set a Bit
x |= ( 1u << 3 ) ; OR forces bit 3 to 1
Every other bit is unchanged
7
6
5
4
3
2
1
0
x
0
1
0
0
0
0
0
1
1 << 3
0
0
0
0
1
0
0
0
mask
x | mask
0
1
0
0
1
0
0
1
bit 3 set
Notes: Rust is identical except the literal: x |= 1 << 3. Turning on an LED or enabling a peripheral is exactly this line.

## Slide 59
Clear a Bit
x &= ~( 1u << 6 ) ; C, C++
x &= !( 1 << 6 ) ; Rust
7
6
5
4
3
2
1
0
x
0
1
0
0
1
0
0
1
~(1 << 6)
1
0
1
1
1
1
1
1
inverted mask
x & mask
0
0
0
0
1
0
0
1
bit 6 cleared
Notes: Invert the mask so it has a 0 only at the bit to clear, then AND. The most common mistake is forgetting the ~ and clearing every OTHER bit.

## Slide 60
Toggle a Bit
x ^= ( 1u << 0 ) ; XOR flips bit 0
Run it twice and you are back where you started
7
6
5
4
3
2
1
0
x
0
0
0
0
1
0
0
1
1 << 0
0
0
0
0
0
0
0
1
mask
x ^ mask
0
0
0
0
1
0
0
0
bit 0 flipped
Notes: The classic blinking LED: toggle the pin, wait, repeat.

## Slide 61
Test a Bit
Shift it down, then keep only bit 0:
( x >> 3 ) & 1 1 or 0
Or mask it in place:
( x & ( 1u << 3 ) ) != 0 true or false
In Rust the second form gives a bool
Notes: Both are common. The parentheses in the second form are not optional in C - next slide.

## Slide 62
The Precedence Trap
if ( x & MASK == 0 )
C, C++ read it as: x & ( MASK == 0 )
always 0 - the test never passes
Rust reads it as: ( x & MASK ) == 0
Always parenthesize bit operations
Notes: In C, == binds tighter than &, a historical accident from before && existed. Rust fixed the order. Parenthesize anyway, so the code reads the same in every language.

## Slide 63
Fields Packed in a Register
One byte, two fields:
bit 7
EN
bit 6
-
bit 5
-
bit 4
-
bit 3
-
bit 2
M2
bit 1
M1
bit 0
M0
enable
mode (0 - 7)
Notes: Hardware control registers look exactly like this. Different bit ranges mean different things, and you use masks and shifts to reach each one.

## Slide 64
Reading and Writing Fields
mode = reg & 0x07 ; low three bits
enable = ( reg >> 7 ) & 1 ; top bit
Change the mode, keep everything else:
reg = ( reg & ~0x07 ) | ( new_mode & 0x07 ) ;
Rust: the same, with ! in place of ~
Notes: The read-modify-write in the middle line is the single most important bit manipulation idiom in embedded programming: clear the field, then OR in the new value.

## Slide 65
Bit Operators on Structs
Members are integers - every bit operator applies:
my_sample.adc_counts & 0x0FFF
keep only the 12 bits a 12-bit ADC produces
my_sample.adc_counts >> 4
drop the 4 noisiest bits
Notes: Tie back to the sample_t running example. Masking to the converter width is a real defensive step when a register returns stray upper bits.

## Slide 66
Bit Operators on Arrays
A simple checksum: XOR every byte together
C, C++:
uint8_t check = 0 ;
for ( int i = 0 ; i < N ; i++ ) check ^= data[i] ;
Rust:
let mut check : u8 = 0 ;
for i in 0..N { check ^= data[i] ; }
Notes: Receiver computes the same XOR; a mismatch means a byte was corrupted. Real protocols use CRCs, which are the same idea with shifts added.

## Slide 67
Precedence in C and C++
Highest
! ~ ++ -- unary
* / %
+ -
<< >>
< <= > >=
== !=
& then ^ then |
&& then ||
= += -= &= |= ...
Lowest
Notes: Note where & sits: below ==. That is the precedence trap from earlier.

## Slide 68
Precedence in Rust
Highest
! - unary
as type conversion
* / %
+ -
<< >>
& then ^ then |
== != < <= > >= cannot chain
&& then ||
= += -= &= |= ...
Lowest
Notes: The bit operators sit ABOVE comparison in Rust, which is what you would expect. When in doubt in any language, use parentheses.

## Slide 69
What We Can Now Do
Arithmetic on variables, members, elements
Comparison values, and whole structs and arrays
Clause logic && || ! on conditions
Bit logic & | ^ ~ << >> on every bit
Seven truth tables describe all of it
Notes: Summary. The ALU from lecture one does every one of these in a single instruction.

## Slide 70
Let's practice
Exercise: Using opspractice
Notes: Lab exercise. Have students predict each result on paper first - division, remainder, overflow, and each bitwise operation - then run it and compare.